Introduction:

Mercury:  Hg, liquid silver, hydragyrum, quicksilver

Mercury is a naturally occurring element.  It is found in the Earth’s crust in an average concentration of about 0.5 parts per million.  It can be found in plants and trees, soil, mineral products, and natural waters.  Because of its unique properties, mercury has been and is used in a variety of industrial and manufacturing processes and consumer products, such as light bulbs, thermometers, mirrors, soap, electric switches, batteries and paints.  Even the health and medical profession utilizes mercury in such things as amalgam dental fillings, contact lense solution, and pharmaceuticals.

Mercury is however, also poisonous and toxic to the human body.  It is readily absorbable by the respiratory tract, skin and intestinal tract.  Spilled and heated mercury is particularly hazardous since mercury can disperse to the air at room temperature.  Exposure to minute amounts may not result in any immediate affect, but continued exposure over time can result in a variety of ailments including those affecting the mental, dental, kidney, muscle and nervous systems.  The mad hatter of Alice in Wonderland fame suffered the affects of mercury poisoning, a common ailment of early hatters who would cure hat brims with a mercuric solution.

Because of its nature, mercury can also concentrate in plants, fish, animals, and humans.  Release of mercury into the air or water by manufacturers or use/disposal of consumer products eventually finds its way to and builds up in the food chain.

While much of the mercury accumulation problem in Maine is related to atmospheric deposition, all inputs of mercury to the environment, for which we have some alternative for control, are worthy of our review and action.

Mercury Pollution Prevention Planning

Mercury P-Miser – a six step program for a cleaner environment

Purchasing

Establish procedures and practices designed to identify actual or potential mercury inputs to you facility.  Such procedures and practices may include:

- Survey of current or future vendors regarding the use of mercury or mercury containing compounds for supplied products/material

- Survey/request analytical data from vendors for supplied bulk materials (to assist in facility profile calculations)

- Establish facility guidelines/ procedures regarding the purchase of mercury containing products or materials.

- Establish minimum acceptable mercury concentrations for raw materials.

Management

Ensure management supported business practices and procedures are established, implemented, and communicated which minimize, reduce, or eliminate actual or potential mercury emissions.  (As practicable)  The establishment of such practices and procedures includes an alternative analysis as well as an evaluation of costs and both social and environmental benefits.

Inventory

Conduct an inventory of facility equipment, processes and materials to determine mercury profile.  Include active and storage areas.

Substitute

Review and evaluate alternatives for mercury containing products.  Substitute where possible.

Education

Educate employees regarding mercury issues.  Consider including sub topic areas such as Environmental/Health concerns, facility practices, and work and home prevention/minimization practices.  Consider livening up the conversation by focusing a portion on areas of common interest to the nature/sport enthusiast about mercury in fish and wildlife for example.

Recycling

Recycle or ensure proper disposal of spent, surplus, or out of service mercury or mercury containing products/materials.

Examples:

- Fluorescent light bulbs

- Batteries

- Electrical switches

- Laboratory reagents

Have some mercury spill kits on hand or strategically placed to properly and safely handle spilled mercury-containing material.

Chemicals/Materials with Varying Amounts of Mercury

Sulfuric Acid – Sulfuric acid is typically produced as a byproduct of certain industrial processes.  Acid produced as a by-product of petroleum refining or nickel smelting have been found to have the lowest mercury content.

Caustic – Caustic can be produced by diaphragm or mercury cell technology.  Since mercury cell technology utilizes mercury in the manufacturing process there is an opportunity for inadvertent contamination.  Accordingly, customers can specify and vendors may certify desired or maximum acceptable mercury specifications.  Also, caustic produced by diaphragm method can have varying mercury concentrations depending on the type or grade produced.  Rayon grade caustic for example, tends to have a higher mercury residual, which is produced with low chlorides for special uses.

Products Potentially Containing

Mercury & Available Alternatives

Product		Alternative

Thermometers		Alcohol based 				thermometers

Thermostats		Electric or alcohol				based thermostats

Barometers		Electric or alcohol				based barometers

Swimming pool	Electric or alcohol

alarms		based alarms

Electrical switches	Non mercury 				containing switches

Dental amalgams	Non mercury 				containing amalgams

Bug Zappers		Citronella, mercury 				free fluorescent/ 				sappers

Fluorescent bulbs/lamps	Mercury free bulbs

neon bulbs/lamps

Homeopathic		Non mercury

medication		containing medication

Antibacterial soap	Non mercury				containing soap

Nasal Spray		Non mercury 				containing spray

Eye cosmetics		Non mercury

containing cosmetics

Contact lens solution	Non mercury				containing solution

Commercial popcorn	Non mercury

poppers		containing poppers

Laptop computer	Non mercury

shutoff screen switches	containing switches

Mercury Industrial Pollution Prevention Primer

A guide for mercury pollution source reduction and minimization.